### Marlin Framework Documentation
#### Recommended Tools for Compiling Marlin
To compile Marlin firmware, it is highly recommended to use Visual Studio Code (VSCode). Unlike other tools, such as Arduino IDE, certain versions of Marlin cannot be compiled using Arduino, and some versions are only compilable on Ubuntu operating systems. However, these limitations do not apply to VSCode, making it the preferred choice for seamless and efficient compilation across different platforms.
#### Setting Up VSCode for Marlin
1. Install Required Extensions
  1. Open VSCode and navigate to the Extensions marketplace.
  2. Search for and install the following extensions:
    1. Marlin Firmware Extension
      1. Provides tools and settings to streamline configuration and compilation of Marlin firmware.
    2. PlatformIO IDE Extension
      1. A crucial tool for building and uploading the firmware, offering compatibility with various microcontroller platforms.
    3. C/C++ Extension
      1. Enables IntelliSense, code navigation, and debugging support for Marlin’s C++ codebase.
2. Open the Marlin Project Folder
  1. From the VSCode menu, click on File > Open Folder.
  2. Select the folder containing the Marlin project files that you have downloaded.
  3. This will load the Marlin project into VSCode, allowing you to configure and compile the firmware.
3. Locate the Configuration Files
  1. Inside the project folder, navigate to the Marlin directory.
  2. Locate the Configuration.h file. This file contains the primary configuration settings for the firmware.
  3. Open Configuration.h in the VSCode editor to begin customizing the firmware for your specific hardware and printer settings.
4. Educational Resources in Configuration.h
  1. In the initial lines of the Configuration.h file, you will find comments with links to various educational websites.
  2. These resources provide detailed explanations and guides for configuring different sections of the Marlin firmware, helping you understand the purpose of each setting and making it easier to customize the firmware for your specific needs.
5. Disabling the Boot Screen
  1. To prevent the Marlin logo from appearing on the display during boot, locate the SHOW_BOOTSCREEN option in Configuration.h.
  2. Comment out the line by adding // at the beginning of the line:
    cpp
    Copy code
    // #define SHOW_BOOTSCREEN
  3. This will disable the boot screen and prevent the Marlin logo from being displayed when the printer starts.
6. Custom Boot and Status Screen Images
  1. To display your custom start-up image (e.g., a logo or a welcome screen), you can enable the SHOW_CUSTOM_BOOTSCREEN and SHOW_CUSTOM_STATUS_SCREEN_IMAGE options.
  2. In Configuration.h, locate and uncomment the following lines:
    cpp
    Copy code
    #define SHOW_CUSTOM_BOOTSCREEN
    #define SHOW_CUSTOM_STATUS_SCREEN_IMAGE
  3. After enabling these options, prepare your custom image as a PNG file and place it in the /marlin/pictures folder within your Marlin project directory.
  4. Ensure that the PNG image is properly formatted and within the size limits supported by your printer's screen.
7. Configuring the Serial Port
  1. To enable simultaneous connection of both the display and the computer to the Marlin firmware, you need to configure the serial port.
  2. In Configuration.h, locate the SERIAL_PORT setting and set it to 1:
    cpp
    Copy code
    #define SERIAL_PORT 1
  3. By setting the serial port to 1, you allow both the display and the computer to be connected to Marlin at the same time, enabling communication between the two devices.
8. Setting the Baud Rate
  1. In this section, we will configure the baud rate for communication between Marlin and the connected devices.
  2. If you are using a Ramp board, the maximum supported baud rate should be set to 115200.
  3. To set the baud rate, locate the BAUDRATE setting in the Configuration.h file and update it as follows:
    cpp
    Copy code
    #define BAUDRATE 115200
  4. This ensures proper communication speed between the firmware and the connected devices, optimizing performance for your setup.
9. Enabling Serial Ports in New Marlin Versions
  1. In newer versions of Marlin, you can enable additional serial ports for communication. However, this is not possible in older Marlin versions.
  2. If you are working with Marlin versions older than 2.0.5, do not enable additional serial ports.
  3. To avoid issues, ensure that only the primary serial port is enabled in older versions by leaving the settings for additional serial ports commented out.
10. Disabling Bluetooth and Wi-Fi
  1. For wireless communication, it is recommended not to enable Bluetooth or Wi-Fi in the Marlin firmware unless specifically required.
  2. These features may introduce complications and are not essential for most users. Instead, if you need wireless communication, consider using an ESP32 module for reliable and robust wireless connectivity.
  3. By not enabling Bluetooth or Wi-Fi in Marlin, you simplify the setup and avoid potential conflicts with hardware and software compatibility.